## Slide 1: COA/CA Project Methodology
Processor Analysis using the SimpleScalar Simulator
Benchmarks Utilized: go.ss, gcc95.ss, and ijpeg.ss
Simulation Tool: sim-outorder executed on Ubuntu via Oracle VM
Roll no: BSEE23038
Roll no: BSEE23016

## Slide 2: Project Workflow
Modified processor, cache, and branch predictor parameters
Executed simulations using sim-outorder
Redirected simulation outputs to .txt files
Extracted required statistics using grep commands
Prepared tables, graphs, and comparative analyses

## Slide 3: Part I Methodology
Benchmarks Selected: go.ss and gcc95.ss
Evaluated Small, Medium, Large, and Excessive cache configurations
Configured cache parameters using -cache:il1, -cache:dl1, -cache:dl2, and -cache:il2 options
Recorded sim_cycle and sim_CPI performance metrics

## Slide 4: Part I Output Analysis
Extracted sim_cycle values using grep sim_cycle
Extracted sim_CPI values using grep sim_CPI
Compared execution cycles and CPI across multiple configurations
Generated graphs with memory model size represented on the X-axis

## Slide 5: Results
For gcc95.ss
Small Processor:

## Slide 6
Medium Processor:
For gcc95.ss
Large Processor

## Slide 7
Excessive Processor:
For gcc95.ss

## Slide 8
For gcc95.ss
Execution Time
CPI
Rest of the Screenshots and Values are shown in Appendix

## Slide 9: Part II(a) Methodology
Compared branch predictors using ijpeg.ss with large.ppm input
Evaluated Bimodal predictor configurations: 512, 1024, and 2048
Evaluated 2-Level predictors with varying history widths and table entries
Implemented Combination predictors integrating Bimodal and 2-Level schemes

## Slide 10: Part II(a) Analysis
Extracted directional hits and miss statistics
Utilized grep commands for bpred_bimod, bpred_2lev, and bpred_comb
Prepared comparative performance tables
Generated branch predictor performance graphs

## Slide 11: Results
Bimodal Size
2-Level Width Comparison

## Slide 12: Results
Combination Predictor

## Slide 13: Part II(b) BTB Methodology
Compared BTB performance using addr_hits statistics
Varied the number of BTB sets
Analyzed different associativity configurations
Compared configurations with a fixed total BTB size

## Slide 14: Results
BTB Associativity
BTB Sets

## Slide 15: Results
Fixed BTB Size
Exact values, given both in excel and appendix

## Slide 16: Part III Methodology
Selected Benchmark: ijpeg.ss
Compared bimod, taken, nottaken, and 2-level branch predictors
Analyzed IFQ size, decode width, and issue width
Compared in-order and out-of-order execution models

## Slide 17: Part III Cache Analysis
Varied Data Cache L1 parameters: nsets, block size, and associativity
Varied Instruction Cache L1 parameters: nsets, block size, and associativity
Extracted cache hit-rate and miss-rate statistics
Plotted cache performance evaluation graphs

## Slide 18: Results
Branch Predictor Comparison
Bimodal Size vs Miss Rate

## Slide 19: Results
IFQ Size vs IPC
Decode Width vs Cycles

## Slide 20: Results
Issue Width vs Cycles
When both IFQ and decode width are changed

## Slide 21: Results
In-order vs Out-of-order
DCache Hit Rate vs nsets

## Slide 22: Results
DCache Hit Rate vs bsize
DCache Hit Rate vs Associativity

## Slide 23: Results
ICache Hit Rate vs nsets
ICache Hit Rate vs bsize

## Slide 24: Results
ICache Hit Rate vs Associativity

## Slide 25: Part IV Methodology
Designed an optimized processor configuration for ijpeg.ss
Constraints Applied: bimod predictor only, in-order issue, and 512B total memory
Allocated 7 shared units among IFQ, decode width, and issue width
Evaluated multiple valid processor configurations

## Slide 26: Part IV Final Selection
Compared sim_cycle values across all evaluated configurations
Selected the processor configuration with minimum execution cycles
Balanced predictor, cache, and pipeline width parameters
Provided detailed justification for the final optimized design

## Slide 27: Results
Chart: 
| IFQ | Decode Width | Issue Width | Total Units | sim_cycle
A | 2 | 1 | 4 | 7 | 1317735
B | 4 | 1 | 2 | 7 | 1320563
C | 4 | 2 | 1 | 7 | 1316840
D | 2 | 4 | 1 | 7 | 1317219
Comparison of Different Configurations

## Slide 28: Results
Comparison of Different Configurations
After comparing the simulation cycles of all tried configurations, we found that Configuration C gave the minimum cycles. Although, the difference was not too significant, C turns out to be the optimum Processor.
Details are as following:
IFQ: 4 Decode Width: 2 Issue Width:1
Sim Cycles: 1316840
All configurations were tried keeping the given constraints in view.

## Slide 29: Conclusion
The project was successfully completed through simulation-based evaluation
Results were validated using tables, graphs, and comparative analyses
The optimal processor configuration was selected based on minimum sim_cycle
SimpleScalar provided comprehensive architectural performance insights

## Slide 30: Key Achievements
• Successfully analyzed processor performance using SimpleScalar
• Evaluated cache and branch predictor configurations systematically
• Compared architectural trade-offs using CPI and execution cycles
• Identified an optimized processor design under given constraints